## Slide 1: 3D Peek Printer
Senior Capstone Design

## Slide 2: 3D Printing Technology
Pros
  Low machine cost
  Low per-unit print cost
  Rapid Production
  Low size footprint
  Wide availability
  High strength
  High temperature
Cons
  Dimensionally inaccurate
    ±0.1mm vs ±0.005mm for CNC
  Limited object size
  Low strength
  Low temperature
In 2018, the 3D printing industry was worth 1.5 billion. It is predicted to be worth 3.78 billion by 2026

## Slide 3: Market Analysis
 | Max Extruder Temp. | Max Bed Temp. | Max Chamber Temp. | Build Volume | Price
Average Commercial PEEK Printer | 490 | 193 | 165 | 5.01e7 | 61,000
Intamsys Funmat HT | 450 | 160 | 90 | 1.76e7 | 6,000
Aon-M2+ | 450 | 200 | 135 | 1.30e8 | 50,000
3DPP | 450 | 200 | 80 | 1.12e8 | 2,500
Intamsys Funmat HT
  10x smaller build volume
  Double price
Aon-M2+
  Similar build volume
  10x price

## Slide 4: Design Requirements
Functional Requirements
Respond to movement commands in the X, Y, Z, and extruder directions
Heat nozzle to 450 °C, bed to 200 °C, chamber to 80 °C
Print all common filament types without heated chamber
Can print PEEK/PSU object
Print volume of 300x280x1330mm
Operate at maximum chamber temperature for 3 days continuously
Usability Requirements
System can operate on a local 20A breaker without heated chamber and with a heated chamber on 3 separate 20A circuits
Will have thermal protection for the nozzle, heated bed, and chamber
System will have fused connections in the event of a short
User Experience Requirements
User can monitor and control temperature and movement locally through an LCD
Through a web interface, the user can:
  Control nozzle, bed, and chamber temp
  Control X, Y, Z, and E movement
  Send commands
  Start, stop, and monitor prints
  View print through real-time stream

## Slide 5: Initial Concept Generation
Cartesian system
Belt/pulley combination with counterweight for Z-axis
Fail-safe latches at top and bottom of printer to prevent bottoming-out
Mount motors outside heated chamber, cool other motors with Peltier Plates
Space heater heating element
Surrounded by insulation

## Slide 6
Preliminary Thermal Analysis
Method 1
Method 2
Pros
Less Volume
Sturdy
Clean
Cons
Worse Insulator
Pros
Better Insulator (larger thickness)
Cons
Flaky
Bulky
3”
1”
¼”

## Slide 7: Next Steps
CAD Frame and Components
Assemble movement system in frame
  Build Z-axis movement mechanism
  Design belt tensioning mechanisms
Get working 3D printer without build chamber
Perform more complete thermal analysis on heating element